## Slide 1: Kickoff example
Create a new file
Site information tab: no to CSW permit, zip=55155, 3 acres impervious, 2 acres turf on B soil
Schematic tab
    Bioretention no underdrain, 1 acre impervious , 3000 ft2 areas, 1.35 feet depth, B soil, 48 hour drawdown
    Bioretention with underdrain, 2 acre turf B soil, 1 acre impervious, underdrain not raised, not lined, 3000 ft2 for each area, overflow depth=1.5 feet, 2 foot media depth, 0.11 FC-WPt, 0.25 MP-FC, no tree, Mix A, no to P test, no amendment, B soil (0.45 in/hr), 48 hr drawdown, route to bioretention with no underdrain
    Infiltration basin, 1 acre impervious, 4000 ft2 areas, 1.8 foot overflow depth, B soils, 48 hour drawdown

## Slide 2: Kickoff example – Results tab
Is the performance goal met
Look at each BMP and the water budget and water routing. How can we meet the performance goal?

## Slide 3: MIDS calculator
An Excel spreadsheet that
  quantifies reductions in stormwater runoff volume for a given BMP or group of BMPs
  quantifies reductions in phosphorus (P) and TSS in stormwater runoff for a given BMP or group of BMPs
  can be used to determine and size best BMP(s) for a particular situation
Has a Graphical User Interface (GUI)

## Slide 4: Why do we want to know these?
Meet regulatory requirements
Meet water quality targets
Choose most efficient/effective BMP

## Slide 5: Performance goals
Targets for volume and/or pollutant reductions
  CSW permit has a goal of 1 inch retention of impervious surfaces for new development: captures about 90% of annual precipitation
  MIDS goal is 1.1 inches: mimics native vegetation and soils
  TMDLs might have goals for TSS or P reduction to meet surface water quality standards
  2 year, 24-hour storm: used for constructed ponds
  Etc.

## Slide 6: Who uses it?
Engineers for project sites
Technical staff at watershed organizations and other Local Government Units (LGUs)
People seeking funding for projects
Educators
Etc. – we can’t track all users, but Version 3 has been downloaded 4500 times since January 2017

## Slide 7: How does it work?
Calculate the amount of stormwater runoff, P, and TSS entering the BMP
Different BMPs have removal efficiencies based on research and monitoring
Calculator does a mass balance on volume, P, and TSS coming in, being removed, and returning as runoff

## Slide 8
100% TSS, PP, DP reduction
Overflow volume
0% TSS, Particulate P (PP),
and Dissolved P (DP)
reduction
Infiltration BMPs
100% TSS, PP, DP reduction
Filtered volume
60% TSS. Particulate P (PP),
and Dissolved P (DP)
Calculated based on media
Filtration BMPs w/ some infiltration
Settled solids
Settled solids
90% TSS and associated pollutants,
No removal of dissolved pollutants
Sedimentation BMPs
No infiltration

## Slide 9
Green Roof
Bioretention Basin
Infiltration Basin
Permeable Pavement
Swale Side Slope
Swale Main Channel
Wet Swale
Swale With Underdrain
The BMPs

## Slide 10
Sand Filter
Stormwater Pond
Stormwater Pond w/ Filter Bench
Wetland
Other
Other
Harvest and Reuse
Impervious Disconnect
Bioretention Basin with underdrain
Tree trench

## Slide 11
Underground Infiltration
Tree trench with underdrain

## Slide 12: Problem 1
2 acre site
  1 acre impervious
  1 acre pervious turf
B soils
Zip = 55155
Goals
  Infiltrate first 1.1 inches off impervious surfaces
  Capture 80 percent of Total P

## Slide 13: Some features
Zip code – rainfall data
Question about CSW permit – affects BMPs available
Default values for retention requirement, P and TSS concentrations
Must have impervious acres
Summary information toolbar

## Slide 14: Warnings and restrictions
Warnings involve a change of a default condition (e.g. changing the P concentration)
Restrictions prevent you from entering data
  Drawdown requirement
  Green roof
  Bioretention depth
  Permeable pavement
  Swale side slope
  Disconnection BMP
  Others

## Slide 15: Help
Links are to pages in the manual

## Slide 16: Treatment train
Multiple BMPs used in series
Route excess water from one BMP to the next

## Slide 17: Problem 2
10 acre site, half is pervious forest and half is impervious
  Impervious: 1 acre on A soils, 2 acres on B soils, 2 on D soils
Goal is to meet the MN Construction SW Permit – infiltrate first 1 inch off impervious surfaces
Consider drawing a site map first; you’ll probably need or want multiple BMPs; include treatment train on your map
Pick your zip code